## Slide 1
Modelling effective refractive index & random cluster (IF NECESSARY)
Scattering codes and input Parameters
Output
bruggeman.f - Bruggeman Mixing rule to determine the effective dielectric function
sccgp.f – random sphere geometry generator
Auxiliary codes
edfb.f – definition of scatterer parameters (dielectric constant, radius, no. of shells, ...)
sph.f & clu.f: scattering code for sphere & cluster, eventually stratified inclu.f: scattering code for a sphere & cluster with inclusions
Plane wave incidence (linear and circular polarization), angular analysis for scattering, average on the orientation of the cluster.
frfme.f: calculus of incident multipolar amplitudes for TEM00 laser beam (linear, radial, azimuthal polarization) in a 3D focal region, based on angular spectrum decomposition
lffft.f: auxiliary code for mounting the outuputs of (1)-(2) and (a)
Principal Codes
1.2.3) Scattering, absorption and extinction cross sections of the scatterer, even averaged. Differential cross sections. Complex scattering amplidudes, Polarization analysis. Angular analysis for the scattering. Optical force and torque for plane wave. Mueller Matrix
1.2.3+a) Optical force and torque for trapped scatterers in a focused laser beam, efficiencies and stiffness in the different points of the 3D grid
Optical Properties & Mechanical Effect
Values of refractive index and filling fractions to determine the effective diel function
Radius for the single monomers that form the random cluster
Input parameters
refractive indices, sphere radius, wavelengths
coordinates of the spheres, incident angles, scattered angles
Numerical aperture of the lens, coverslip distance, definition of the 3D-grid for the calculus of force near the nominal focus
Input Parameters

## Slide 2: How scattering code works: the case of a single sphere
SPH.f
Edfb.f
Formatted
Input data
DEDFB
Unformatted
Output
TEDFB
Formatted
Output
OEDFB
Formatted
Input data
DSPH
Formatted
Output
OSPH
Unformatted
Output
TMMS
The info on refractive index/dielectric constants, can be given in DEDFB using:
the output of bruggeman.f job for mixture
Experimental data from ellipsometric measurements
Some specific models implemented in the code (Drude model, Lindhard model, damped-oscillator model for dielectric…)
Wavelenghts
Dielectric constant of the environment
Radius of the sphere,
no. of shells & dielectric constants of the single layer
Polarization type of the incident field
Values of truncation for multipolar expansions
Scattering geometry: incident and scattering angles
The file contains all the usefull informations on the properties of the sphere, and constitute an input unformatted file for sph.f.
The file contains all elements of T-matrix for the studied case, and constitute an input file for the trapping issue and other specific jobs.

## Slide 3: How scattering code works: the case of a cluster
CLU.f
Edfb.f
Formatted
Input data
DEDFB
Unformatted
Output
TEDFB
Formatted
Output
OEDFB
Formatted
Input data
DCLU
Formatted
Output
OCLU
Unformatted
Output
TMMS
The info on refractive index/dielectric constants, can be given in DEDFB using:
the output of bruggeman.f job for mixture
Experimental data from ellipsometric measurements
Some specific models implemented in the code (Drude model, Lindhard model, damped-oscillator model for dielectric…)
Wavelenghts
Dielectric constant of the environment
Number of spheres
Radius of the spheres,
no. of shells & dielectric constants of the single layer for the different spheres
Polarization type of the incident field
Values of truncation for multipolar expansions
Scattering geometry: incident and scattering angles
Cartesian Coordinates of the spheres constituting the cluster: in case of a random geometry we use the coordinates given by sccgp.f job
The unformatted file contains all the usefull informations on the properties of the spheres constituting the cluster, and is an input file for clu.f.
The unformatted file contains all elements of T-matrix for the studied case, and is an input file for the trapping issue and other specific jobs.

## Slide 4: How trapping routines work
FRFME.f
Unformatted
Input
TEDFB
Unformatted
Input
TMMS
Formatted input DFRFME
Formatted output OFRFME
Unformatted output TFRFME
The angular spectrum representation
The file contains all the multipolar coefficients of the incident field, and constitute an input unformatted file for lffft.f.
Width of the trapping region
Number of points of the mesh of the 3D trapping region
Numerical aperture of the focused lens
Possibility to inctroduce the lens aberration
lffft.f
Formatted input
DLLLFT
Formatted output OLLLFT
Fort.66
Fort.99
X-Y-Z Coordinates of the 3D-trapping region
Cartesian components of trapping force
Fort.67
Cartesian components of optical torque